## Slide 1: External validation of a novel landmark-based deep learning automated tibial slope measurement algorithm applied on short radiographs from ACL injured patients
Results
Two-hundred and eighty-nine radiographs were included in the study and therefore analyzed both by the manual and the automated method. A mean tibial slope of 9.7° (SD 2.7°, Range 3.0° – 19.1°) was found. The interrater and intra-rater measurement between the independent measurers for the two-circle method was
0.86 and 0.92. Further, the intra-rater agreement of the model was 1.00, while an ICC between 0.73 and 0.8 was found for the inter-rater reliability (as comped to manual). Time consumption for a manual reading was 52.5 while automated readings took 28.2 seconds.
R. Kyle Martin, Sanna Håland, Sung Eun Kim, ByeongYeong Ryu, Jun Woo Nam, Du Hyun Ro, Andreas Persson, Eivind Inderhaug
Sanna Håland University of Bergen sanna.haland@student.uib.no
Background
Deep learning algorithms can aid medical decision-making by performing routine tasks without any human bias.
Reading of standardized radiographs lend itself well for a computerized approach. Posterior tibial slope is increasingly recognized as a factor in lower leg biomechanics. Slope readings should therefore be readily available when considering knee ligament or knee replacement surgery.
Purpose and aim
The current study aims to externally validate a deep learning model developed for posterior tibial slope readings by applying an independent dataset, not included in initial development, for testing of reliability of
the model – compared to human
performance testing. The hypothesis was that a computerized approach would yield a reliability that leveled human analyses.
Methods
A consecutive series of lateral knee radiographs from patients undergoing ACL-surgery were eligible for inclusion. Two independent experienced clinicians individually assessed the tibial slope measurement to establish the intra-reader reliability. Further all images were processed by the newly developed model for the automated readings. Intra-rater and inter-rater reliability were thereafter established between readers and between manual and the automated readings measured by inter- and intraclass correlation coefficients (ICC). Time consumption between methods were noted.
Extreme differences between the two methods were analysed for potential errors.
ACKNOWLEDGEMENTS
I would like to thank my supervisor Eivind Inderhaug for his counselling in this
project. Also, I would like to thank Dr.Martin, University of Minnesota, University of
Seoul and Andreas Persson for the collaboration. In addition I would like to thank my research group STAR for their counselling.
Figure 1 – Manual measurement of the slope applying the 2-circle method
Figure 2 – Automated measurement of the posterior tibial slope on a short lateral knee radiographs
Figure 3 – Bland Altman plot comparing manual measurements and Connecteve 3A measurements.
Conclusion
In this external validation of a newly developed model for automated readings of tibial slope measures – a perfect intra-rater reliability and a good inter-rater reliability was seen. Although the model needs some further refinement in reporting the tibial slope as compared to a gold standards manual measurement, it clearly demonstrates the elimination of human error with repeat readings and less time consumption as compared to human effort.